## Slide 1: Prediction of Shear and Flexural Strength of Reinforced Recycled Aggregate Concrete Beam: Machine Learning Approach
Nandita Kamath, Subhasis Pradhan and Sudhirkumar V. Barai

## Slide 2
Growth in Population and Economy
Industrialization and Urbanization
Huge amount of construction work
Depletion of natural resources
Construction and Demolition Waste
Concrete
Natural Aggregate
C&D
Waste
Background

## Slide 3
Background
India invests around 10% of the GDP on construction activities.
Central Pollution Control Board, Ministry of Environment, Forests & Climate Change, India
  Approximately 25 to 30 million tonnes of C&D waste is generated in India and only 5% of which is processed to extract RA.
Approximately 70% to 80% of its total volume of concrete is occupied by aggregates.
IS: 383 (2016) suggests for the replacement of RCA upto
  100% lean concrete
  20% plain concrete
  25% reinforced concrete

## Slide 4
The aggregate yielded by crushing of waste parent concrete is known as Recycled Aggregate (RA).
The concrete in which natural aggregate is replaced partially or fully by RA is known as Recycled Aggregate Concrete (RAC).
Background
Waste concrete (C&D waste)
Recycled coarse aggregate (RCA)
Recycled fine aggregate (RFA)
Recycled aggregate (RA)

## Slide 5
Questions to be Addressed
1- Can we prepare structural concrete using 100% recycled coarse aggregate (RCA)?
2- How to design the recycled aggregate concrete (RAC) mix with 100% RCA?
3- How is the mechanical performance of RAC got affected?
4- Does it affect the performance of structural members (beam, column and slab)?

## Slide 6
Process to Address the Questions
Material Processing and Its Characterization
Recycling Process of RCA
Characterisation of RCA
Mix Proportioning and Mixing Approach
Mix Design Method
Performance Evaluation of Concrete
Beam
Column
Structural Applications
Fresh Stage
Hardened Stage
Macro Level
Slab
Life Cycle Assessment and Cost Analysis
Mixing Approach
Fracture Behaviour
Micro and Meso Level

## Slide 7
Particle Packing Method (PPM)
Particle Packing Method (PPM) is a process of optimization of aggregate proportion in the mixture.
Smaller particles fill up the voids between large particles.
This study could serve as the thumb rule for mix design of RAC with improved mechanical properties.
Coarse aggregateL
Coarse aggregateS
Cement paste
Fine aggregate

## Slide 8
Database of RAC Beams without Shear Reinforcement (91 data)
Database of RAC Beams with Shear Reinforcement (96 data)
Database
Where, = RCA replacement percentage, = width of the beam, = effective depth of the beam, = total depth of the beam, = maximum size of RCA, = longitudinal reinforcement content, = yield strength of longitudinal reinforcement, = compressive strength of concrete (28 days), = total length of the beam, = effective span of the beam, = shear span of the beam, = shear span to depth ratio, = ultimate strength of the beam, = shear reinforcement content, = yield strength of shear reinforcement, = cracking strength of beam, = yield strength of beam.
Database of RAC Beams without Shear Reinforcement
Database of RAC Beams with Shear Reinforcement

## Slide 9
RAC Beams without Shear Reinforcement
Derived Expressions for Ultimate Strength Prediction
RAC Beams with Shear Reinforcement
 Average value 1.08 and CoV 0.17
 Average value 1.14 and CoV 0.14

## Slide 10
Application of Machine Learning

## Slide 11: Model Development & Project Workflow
Define Objectives
Data Preparation
Feature Analysis
Model Building
Model Evaluation
To Predict Shear Strength of RAC Beams with/without Shear Reinforcement
Data Wrangling to flag outliers
Statistical Data Analysis to gauge spread of data (Mean/Median/Range)
Updating any missing values and removing unwanted variables
Analysis of all Input Parameters that affect Target Variable
Data Exploration to Categorize Input Features (Categorical/Continuous Variable)
Correlation Plot to determine relation between continuous variables.
Selection of most relevant features with respect to target variable
Randomly Splitting Data into Training & Testing Sets
Selecting Supervised ML algorithms
Calculate mathematical efficiency of model to estimate performance:
Coefficient of Determination
Root Mean Squared Error
Mean Absolute Error
Root Relative Squared Error

## Slide 12
Database of RAC Beams without Shear Reinforcement (91 data) – Database 1
Database of RAC Beams with Shear Reinforcement (96 data) – Database 2
Database
Where, = RCA replacement percentage, = width of the beam, = effective depth of the beam, = total depth of the beam, = maximum size of RCA, = longitudinal reinforcement content, = yield strength of longitudinal reinforcement, = compressive strength of concrete (28 days), = total length of the beam, = effective span of the beam, = shear span of the beam, = shear span to depth ratio, = ultimate strength of the beam, = shear reinforcement content, = yield strength of shear reinforcement, = cracking strength of beam, = yield strength of beam.
Database of RAC Beams without Shear Reinforcement
Database of RAC Beams with Shear Reinforcement

## Slide 13
Visual Exploratory Data Analysis
Distribution of the predictor variables for Database 1

## Slide 14
Visual Exploratory Data Analysis
Distribution of the predictor variables for Database 2

## Slide 15
The Database consists of predictor (input) variables pertaining to beam characteristics and the target (output) variable, Shear Strength of RAC beam.
Since the Target Variable is available and continuous, a Supervised Regression model is chosen.
Determination of Learning Approach

## Slide 16
The existing dataset is shuffled, selected at random and divided 2 sets; Training and Testing with a 70-30% ratio. The training set is used to build the model and the testing set is used to validate it.
Splitting of Dataset

## Slide 17
Framework ML Model – RAC Beams without Shear Reinforcement

## Slide 18
Framework ML Model – RAC Beams with Shear Reinforcement

## Slide 19
ML Models Trained

## Slide 20
Common Evaluation Metrics for Supervised Learning
Model Evaluation

## Slide 21
Without Shear Reinforcement
Heat maps of correlation matrix are plotted to determine the relation of input parameters on target variable – shear strength
A negative correlation indicates an inversely proportional relation (downward trend)
A positive correlation indicates a directly proportional relation (upward trend)
Absolute correlation value closer to 1 indicates high intensity of relation.
A dark blue or red color indicates high correlation.
Feature Analysis
Without Shear Reinforcement

## Slide 22
Beam size followed by the ratio of a/d effects shear strength the most. This result was also found by Shahnewaz and Alam, from the study of Meta-model of Optimal Prognosis to identify the important parameters.
Validation with Existing Literature (Dataset – 1)

## Slide 23
Longitudinal reinforcement ratio followed by beam size effects shear strength the most. This result was also found by Rahman & Ahmed while predicting shear strength of steel fiber reinforced concrete beams.
Validation with Existing Literature (Dataset – 2)

## Slide 24
R-Squared, RMSE, MSE & MAE scores have been
calculated to understand the performance of each model
However, for regression models, R-Squared and RMSE
scores are considered to select an efficient model
NOTE:
Both Linear Regression and Gradient Boosting offer very high and close accuracy for the dataset.
This explains lowest MAE value for Gradient Boosting
Linear Regression Model gave highest accuracy of 94.2%
MODEL | R2 | RMSE | MSE | MAE
Linear Regression | 0.943 | 19.24 | 370.18 | 16.17
L2 (Ridge) Regression | 0.938 | 20.07 | 402.80 | 16.71
L1 (Lasso) Regression | 0.92 | 26.00 | 676.00 | 21.25
Support Vector Machine (Linear Kernel) | -0.092 | 73.95 | 5468.60 | 60.53
Support Vector Machine (RBF Kernel) | 0.003 | 80.25 | 6440.06 | 66.33
Decision Tree | 0.466 | 58.72 | 3448.04 | 32.27
Multi Layer Perceptron Regression (ANN) | -0.17 | 62.68 | 3928.78 | 43.71
Random Forest | 0.896 | 24.66 | 608.12 | 17.06
Gradient Boosting | 0.93 | 21.73 | 472.19 | 13.95
AdaBoost | 0.773 | 21.82 | 476.11 | 17.20
Chart: Coefficient of Determination
| Linear Regression | Ridge Regression | Lasso Regression | SVM - Linear Kernel | SVM - RBF Kernel | Decision Tree | Random Forest | Gradient Boosting | AdaBoost
R2 | 0.943 | 0.938 | 0.92 | 0 | 0.003 | 0.466 | 0.896 | 0.93 | 0.773
Accuracy Scores for RAC Beams with Shear Reinforcement

## Slide 25
Gradient Boosting Model gave highest accuracy of 93.5%
MODEL | R2 | RMSE | MSE | MAE
Linear Regression | 0.905 | 17.79 | 316.48 | 13.37
L2 (Ridge) Regression | 0.907 | 17.67 | 312.23 | 13.23
L1 (Lasso) Regression | 0.907 | 17.63 | 310.82 | 13.47
Support Vector Machine (Linear Kernel) | 0.626 | 24.76 | 613.06 | 20.19
Support Vector Machine (RBF Kernel) | -0.117 | 61.1 | 3733.21 | 46.01
Decision Tree | 0.878 | 19.88 | 395.21 | 12.44
Random Forest | 0.895 | 17.93 | 321.48 | 12.54
Gradient Boosting | 0.916 | 16.87 | 284.60 | 10.55
AdaBoost | 0.904 | 18.41 | 338.93 | 13.47
Chart: Coefficient of Determination
| Linear Regression | Ridge Regression | Lasso Regression | SVM - Linear Kernel | SVM - RBF Kernel | Decision Tree | Random Forest | Gradient Boosting | AdaBoost
R2 | 0.905 | 0.907 | 0.907 | 0.626 | 0 | 0.878 | 0.895 | 0.916 | 0.904
Accuracy Scores for RAC Beams without Shear Reinforcement

## Slide 26
The selected model is applied on testing set and results are plotted
Scatter plot of Original and Predicted values form a slope very close to 45.
Chart: Original vs Predicted values of Shear Strength in RAC beams without reinforcement
| 42.5 | 104 | 168.7 | 117.5 | 171.8 | 126.1 | 36.4 | 31.1 | 108.9 | 21.4 | 58.94 | 42.5 | 46.95 | 72.900000000000006 | 186.7 | 148.6 | 89 | 21.7 | 96.4 | 91.75 | 38 | 45.05 | 103.9 | 49.07 | 256.60000000000002 | 19.7 | 107.8 | 39.9
predicted_values of Vu (kN) | 46.304 | 79.3439 | 142.0743 | 118.0184 | 144.8787 | 127.0035 | 41.0943 | 27.4685 | 133.5462 | 21.7601 | 59.123 | 47.2102 | 49.4405 | 62.7168 | 148.6206 | 140.8022 | 85.8917 | 20.8094 | 133.0535 | 106.8624 | 41.0943 | 47.3402 | 96.3727 | 50.1193 | 257.1164 | 20.7712 | 153.1194 | 41.0943
Chart: Original vs Predicted values of Shear Strength in RAC beams with reinforcement
| 166.22 | 177 | 163.4 | 20.2 | 105.4 | 54.45 | 27 | 71.5 | 56.67 | 164 | 327 | 67.33 | 42.65 | 80.67 | 83 | 142.6 | 233.6 | 186.5 | 302.82 | 58.4 | 18.8 | 27.1 | 118.5 | 57.35 | 110.55 | 189.5 | 156.9 | 31.95 | 169
predicted_values of Vu (kN) | 188.2628 | 201.4994 | 183.5022 | -2.8855 | 87.8557 | 71.4921 | 32.8025 | 83.1867 | 46.7041 | 194.6766 | 327.1634 | 56.7014 | 51.7847 | 69.6455 | 87.0181 | 173.2365 | 203.49 | 199.6145 | 311.6362 | 98.9812 | -4.1645 | 25.8488 | 119.9178 | 70.6265 | 89.4094 | 197.2656 | 184.9273 | 28.0093 | 197.5436
Validation

## Slide 27
Based on the database, this work developed models using Linear regression, Ridge Regression, SVM – (Linear and RBF kernel), Decision Tree, Neural Network, Random Forest, Gradient Boosting and AdaBoost.
Gradient Boosting model gave the highest accuracy of 93.5% to predict shear strength of RAC beams without shear reinforcement.
Linear Regression gave the highest accuracy of 94.2% to predict shear strength of RAC beams with shear reinforcement.
Beam size and the shear span to depth ratio () affect shear strength the most for RAC beams without shear reinforcement.
For RAC beams with shear reinforcement, longitudinal reinforcement ratio followed by beam size affect shear strength the most.
Conclusions

## Slide 28
References
Cheng, M. Y., Chou, J. S., & Cao, M. T. (2017). Nature-inspired metaheuristic multivariate adaptive regression splines for predicting refrigeration system performance. Soft Computing, 21(2), 477-489.
Gandomi, A. H., Alavi, A. H., Mohammadzadeh Shadmehri, D., & Sahab, M. G. (2013). An empirical model for shear capacity of RC deep beams using genetic-simulated annealing. Archives of Civil and Mechanical Engineering, 13(3), 354-369.
Kara, I. F. (2011). Prediction of shear strength of FRP-reinforced concrete beams without stirrups based on genetic programming. Advances in Engineering Software, 42(6), 295-304.
Pérez, J. L., Cladera, A., Rabuñal, J. R., & Martínez-Abella, F. (2012). Optimization of existing equations using a new Genetic Programming algorithm: Application to the shear strength of reinforced concrete beams. Advances in Engineering Software, 50, 82-96.
Zhang, T., Oehlers, D. J., & Visintin, P. (2014). Shear strength of FRP RC beams and one-way slabs without stirrups. J. Compos. Constr, 18(5), 04014007.
Rahman, J., Ahmed, K. S., Khan, N. I., Islam, K., & Mangalathu, S. (2021). Data-driven shear strength prediction of steel fiber reinforced concrete beams using machine learning approach. Engineering Structures, 233, 111743.
Pradhan, S., Kumar, S., & Barai, S. V. (2018). Shear performance of recycled aggregate concrete beams: An insight for design aspects. Construction and Building Materials, 178, 593-611.
Wakjira, T. G., Ebead, U., & Alam, M. S. (2022). Machine learning-based shear capacity prediction and reliability analysis of shear-critical RC beams strengthened with inorganic composites. Case Studies in Construction Materials, 16, e01008.
Shahnewaz, M., & Alam, M. S. (2020). Genetic algorithm for predicting shear strength of steel fiber reinforced concrete beam with parameter identification and sensitivity analysis. Journal of Building Engineering, 29, 101205.

## Slide 29
Thank you!!!